## Slide 1: Adding the Superset Adder to the DesignWare IP Library
Stevo Bailey

## Slide 2: Motivation
Technology scaling exacerbates variation and reliability issues
Memory circuits have redundancy and error detection/correction schemes
Need arises for robust arithmetic datapaths
Redundancy, reconfiguration

## Slide 3: Addition in Circuits
A3 B3
A2 B2
A1 B1
A0 B0
G3 P3
G2 P2
G1 P1
G0 P0
G3:2 P3:2
G1:0 P1:0
G3:0 P3:0
Setup
CLA (Prefix) Blocks
(G1:0, P1:0) = (G1 + P1G0, P1P0)
Prefix Operation:
A3 B3
A2 B2
A1 B1
A0 B0
FA
S3
S1
S2
Cout
S0
Ripple Carry Addition Delay:
O(N)
FA
FA
FA
Si = Gi-1:0 XOR Pi
Sum Calculation (not shown):
Minimum Parallel Prefix Delay:
O(log2N)
Cin
Notes: Mention how tree is just calculating Cout; similar trees exist for each sum
Mention logic depth of each adder (4 for ripple, 2 for cla)

## Slide 4: Parallel Prefix Adders
Kogge-Stone
Han-Carlson
Brent-Kung
Trade logic depth (delay) for complexity (area and power)
Radix 2, fan-in 2

## Slide 5: Superset Adder
Full Tree
Full controllability over prefix nodes

## Slide 6: Synopsys Overview
Module Compiler Code
Module Compiler
Optimized VHDL
Analyze VHDL in DC
Synthetic Library Code
Add to DC Synthetic Library Path

## Slide 7: Module Compiler Input and Synthesis
MCL Code
Module Compiler Analysis

## Slide 8: Module Compiler Output
Module Compiler Output Files
Module Compiler Output VHDL

## Slide 9: Module Compiler Relative Placement
Relative Placement View (manual)

## Slide 10: Area Comparison
Chart: Area comparison of superset vs. traditional adders
| 8 | 16 | 32
Superset | 1704 | 4465 | 11207
Kogge-Stone | 589 | 1388 | 3248
Brent-Kung | 463 | 955 | 1947

## Slide 11: Delay Comparison
Chart: Critical delay comparison of superset vs. traditional adders
| 8 | 16 | 32
Superset | 1.25 | 1.63 | 2.04
Kogge-Stone | 0.48 | 0.61 | 0.73
Brent-Kung | 0.59 | 0.83 | 1.09

## Slide 12: Design Compiler Code
Synthetic Library Code
TCL Script

## Slide 13: Design Compiler
8-bit Superset Adder Schematic

## Slide 14: Design Compiler
8-bit Superset Adder Schematic

## Slide 15: Current Issue
How do I get VCS to simulate my adders when they include library components?

## Slide 16
Questions?